## Slide 1: Device Model Summary Model ID = dtmi:com:Microchip:AVR_IoT_WM;1 File Name = avr_iot_wm-1.json
Type | Name | Schema | Example JSON Message/Format
Telemetry | temperature | double | {“temperature”:23.752}
Telemetry | light | integer | {“light”:5150}
Telemetry | button_event | Object | {“button_event”:{“button_name”:“SW1”,“press_count”:2}}
Property (Read-Only) | led_blue | Enum | {“led_blue”:1}
Property (Read-Only) | led_green | Enum | {“led_green”:2}
Property (Read-Only) | led_red | Enum | {“led_red”:3}
Property (Writable) | led_yellow | Enum | {“led_yellow”:{“ac”:200,“av”:69,“ad”:“OK”,“value”:2}}
Property (Writable) | telemetryInterval | integer | {“telemetryInterval”:{“ac”:200,“av”:55, “ad”:“accepted”,“value”:20}}
Command (Request) | reboot | Object | {“delay”:“PT5S”}
Command (Response) | reboot | Object | {“status”:“success”,“delay”:5}
Command (Request) | echoMsg | Object | {“echoMsgString”:“Hello, Ronwell”}
Command (Response) | echoMsg | Object | {“echoMsgString”:“Hello, Ronwell”}